## Slide 1
Mobile Computing Presentation
AD HOC ON-DEMAND DISTANCE VECTOR(AODV) ROUTING

## Slide 2
Content
01
02
03
04
05
Introduction
How it works
Types of routing in AODV
Compare AODV and other routing protocols
Advantages and disadvantages

## Slide 3
SCCI/00617/2021 – FELIX KEMBOI
SCCI/00605/2021 – FELISTUS KIOKO
SCCI/00611/2021 – RASHID ISAAK
SCCI/00616/2021 – BRIAN KANOTI
SCCI/00606/2021 - EMMANUEL MUSOLOMI
SCCI/00609/2021 – COLLINS KIBET
SCCI/00612/2021 – CHRISTOPHER OBEGI
Group 6 members

## Slide 4: INTRODUCTION
Ad Hoc On-Demand Vector Routing (AODV) protocol [36] is a reactive routing protocol for ad hoc and mobile networks that maintains routes only between nodes which need to communicate. The routing messages do not contain information about the whole route path, but only about the source and the destination. Therefore, routing messages do not have an increasing size. It uses destination sequence numbers to specify how fresh a route is (in relation to another), which is used to grant loop freedom.

## Slide 5
How it works
It is a reactive routing protocol; it establishes a route to a destination only on demand.
It operates on-demand, establishing routes only when nodes need to communicate which helps conserve resources and reduce network overhead.
AODV works by discovering route-demand, which means it only initiates route requests when a sender node wants to communicate with a destination node. Nodes listen for request and reply packets and maintain routing info for active routes, discarding outdared information to reduce the overhead
AODV is a routing protocol for MANETs(mobile ad hoc networks) and other wireless ad hoc networks

## Slide 6
the devices that are not on a particular path do not maintain routing information nor do they participate in the routing table exchanges.
When a source requires sending a message to a destination and does not have a valid route to the latter, the source initiates a route discovery process.
  Source sends a route request(RREQ)packets to all its neighbors, the latter sends the request to all their neighbors, and so on, until either destination or an intermediate mobile(node)with a “fresh enough” route to the destination is reached

## Slide 8
The above figure illustrates the propagation of the broadcast request(RREQs) across the network.
  each node has a unique sequence number and a broadcast ID, which is incremented each time the node initiate a RREQ
The broadcast ID, together with the IP address of node, uniquely identifies every RREQ
  Intermediate mobile reply only if they have a route to the destination with a sequence number greater than or at least equal to that contained in the RREQ. To optimize the route performance, intermediate nodes record the address.

## Slide 9
From the above figure, since RREP (route reply packet) travels back to the reverse path, the nodes on this path set up their forward route entries to point to the node from which RREP had just be received.
These forward route records indicate the active forward route. The RREP continues traveling back along the reverse path till it reaches the initiator of the route discovery.

## Slide 10
Types of routing in AODV
Route Request (RREQ) – is responsible for discovering of route from source to destination. A node initiates to send/transmit a packet but does not know how to reach the destination. It therefore sends RREQ multicast message to start the route discovery process.
Route Response (RREP) – sends back the route information response to its source. The destination node replies through this packet. If an intermediate node knows the path to the destination, it sends the RREP in response to the RREQ. This allows bode to enter an established route.
Route Error (RERR) – since AODV has less overhead than the proactive protocol, in the event of an interruption (the part no longer functions and hence no messages sent), a RERR message is sent through a node detecting the link interruption. The message is then re-cast by other nodes. The RERR messages shows the unattainable destination.

## Slide 11
Advantages of Ad-hoc On Demand Distance Routing Vector
⦁ No loop generation. This is because of the loop detection and prevention mechanisms as well as route maintenance.
⦁ Reduced overhead. AODV initiates route discovery only when it needs to communicate hence reducing the unnecessary control message (overhead).
⦁ Scalability since there is no loop generation. The network can be scaled easily as there is little worry about loops in the network.
Disadvantages of Ad-hoc On Demand Distance Routing Vector
⦁ A delayed protocol due to route-discovery process, route request flooding and other network dynamics.
⦁ AODV may also take a long time to build the routing table.
⦁ AODV consumes a large share of the bandwidth.

## Slide 12
AODV | DSR
Uses destination routing approach (hop by hop routing) | Uses source routing approach
Requires only one route per destination | Requires multiple routes per destination
Has a small packet header size | Has a larger packet header size
Has low storage space | High storage space
Supports multicast | Does not support multicast
Has moderate routing overhead | Incurs higher routing overhead
Is based on timer activities | Does not rely on any timer-based activities
Comparison between AODV (Ad-hoc On-Demand Distance Vector) and DSR (Dynamic Source Routing) routing protocols.